## Slide 1: Week 2 Presentation
11107014
林冠良

## Slide 2: ADC
A system that converts an analog signal or physical voltage values into a digital signal.

## Slide 3: Analog Digital Converter
Sampling rate: how long does the signal gets converted
Resolution: how precise does the signal gets converted
Modes:
  Single Conversion Mode
  Continuous Conversion Mode
  Scan Mode
  Discontinuous Mode

## Slide 4: UART
A hardware device for asynchronous serial communication in which the data format and transmission speeds are configurable.

## Slide 5: Universal Asynchronous Receiver/Transmitter
Transmit data asynchronously.
Adds start and stop bits to the data packet being transferred.
Two UARTs communicate directly with each other.
Transmit process
  Transmitting UART converts parallel data from a device into serial form.
  Transmits it in serial to the receiving UART.
  Then converts the serial data back into parallel data for the receiving device.

## Slide 6: Packet
Start bit
  Transmission line is normally high when it’s not transmitting data.
  To start a transmission, transmitting UART pulls transmission line from high to low.
Data frame
  5 bits to 8 bits, 9 bits if no parity bit is used.
Parity
  Represent the evenness or oddness of the data.
Stop bits
  The sending UART drives the data transmission line from a low voltage to a high voltage for at least two bit durations indicates the end of the data packet.

## Slide 7: Circuit
Variable resistor(in series)
  Orange: GND
  Green: A0(ADC1)
  Yellow: 3.3V
ST-Link
  RX: TX pin on board(PC4)
  GND: GND pin on board

## Slide 8: Coding
ADC_to_UART

## Slide 9: ADC_to_UART
Enable ADC1
  Mode: IN0
  Resolution: 12 bits
Enable USART1
  Mode: Asynchronous
  Baud rate: 115200 bits/s
Redefine PUTCHAR_PROTOTYPE for fputc() in printf()
Start ADC and Wait for conversion
Retrieve ADC read and calculate voltage value and transmit to UART using printf()

## Slide 10: ADC_to_UART
Voltage conversion
  actualVoltage = adcVariable / (adcResolution / systemVoltage)

## Slide 11: Thank you for your listening
林冠良
Noah_Lin@wistron.com
https://github.com/popshia